## Slide 2
Extending the Life of Your Roof
Roof Asset Management
Fall Protection
Building Code, R Value, and Good Roofing Practices
Technology and Capabilities
Dayton IFMA
Key Points

## Slide 3: Extending the Life of your Roof
Roof Preventative Maintenance Programs
  Annual or Semi-Annual roof inspections

## Slide 4: PREVENTATIVE MAINTENANCE PROGRAM
The National Roofing Contractor’s Association along with major roof manufacturers, recommend adopting a Roof Management Program (RMP). It is a comprehensive preventative maintenance plan that extends the service life of your roof well beyond the warranty. It is also beneficial in extending the life of any other existing roofs that you may have.
It is recommended to have Annual or Semi-Annual inspections to evaluate the conditions of your roof.
Roof evaluations should include a detailed analysis of all roof components, identifying potential problems and damage.
Following the evaluation, a written report along with photographs should be provided.

## Slide 5: Inspect entire roof area for damage that may have resulted from foreign objects or from human activity

## Slide 6: Remove all debris that may have accumulated on the roof surface to ensure it does not restrict drainage

## Slide 7: Inspect and clean all roof drains, overflow drains, gutters and scuppers

## Slide 8: Inspect the entire roof area

## Slide 9: Inspect skylights

## Slide 10: Inspect roof membrane

## Slide 11: Inspect edge securement

## Slide 12: Edge securement failing allowing roof to be blown off

## Slide 13: Inspect HVAC units and fans

## Slide 14: Overview pictures provide the overall condition of the roof

## Slide 15: SAMPLE INSPECTION REPORT

## Slide 16
“Proactive roof maintenance extends the lifetime of your roof by 30%-100%”
National Roofing Contractors Association Claims

## Slide 17
Reduce emergency expenses- travel time costs, temporary repairs, multiple trips
One year guarantee protection
Limit potential liabilities
Costly interruptions of operations
It Makes $ense

## Slide 18
QUESTIONS ?

## Slide 19: Understanding Your Warranty
Your roof warranty specifies
  Type of roof system
  Duration of coverage
  Warranty Number
  Terms, Conditions and Limitations
  Manufacturer’s contact info

## Slide 20
Field sheets, flashings, components provided by manufacturer
Material defects
Workmanship
What the typical manufacturer’s warranty covers

## Slide 21
ON-SITE INSPECTION
REVIEWING WALL DETAILS TO COMPLY WITH MANUFACTURER’S SPECIFICATIONS

## Slide 22: WARRANTY REPAIRS
VOIDS IN SEAMS BEING REPAIRED

## Slide 23: WARRANTY REPAIRS
All repairs completed per manufacturer’s specifications

## Slide 24: Typical Warranty Exclusions
Foot traffic
Third Party Damage
Acts of God
Structural movement
Alterations to roof that do not meet specs
Use of products not provided by manufacturer
Condensation/Moisture entering the roof system

## Slide 25: WARRANTY EXCLUSION PICTURES

## Slide 26: Maintaining a Valid Warranty
Perform regular inspections and maintenance

## Slide 27: Warranty Repairs
When a leak occurs on your roof that is under warranty
  Contact Manufacturer via phone, fax, or email. Then they will contact installing contractor.
  OR
  Contact your preferred contractor directly for a timely response. Elite contractors have a relationship with the Manufacturers that allows them to make service calls on our warranty roofs prior to processing the paperwork.
Contractor’s repair procedure
  Check roof area for defects
  Document and photograph all items found
  Indentify area of leak on aerial view/hand drawing of facility
  Fill out required paperwork for manufacturer; submit pictures and aerial view

## Slide 28: Original Installing Contractor
“It’s not a life sentence”
  Warranties can be transferred from one contractor to another at the request of the building owner.

## Slide 29
QUESTIONS ?

## Slide 30
Roof Asset Management
A Pro-Active Approach of developing a long term cost effective roofing plan

## Slide 31: Roof Asset Management
Planning and budgeting are critical factors of successful property management

## Slide 32: Life Cycle of Your Roof
Life Cycle of Your Roof

## Slide 33: Identify & Prioritize
Accurately identify large expenditures in advance
Develop multi-year budget/roof plan
Prioritize critical areas
Have a complete plan for the life cycle of your facility

## Slide 34: ROOF ASSET MANAGEMENT
Multi-Year Budget/Roof Plan

## Slide 35
We worked with this company to establish a 3-year roofing plan that met their budgetary goals.

## Slide 36: Business Strategy
Corporate America treats their facilities like an asset
They manage their roofs just like the rest of their valuable assets
No longer an “out of sight, out of mind” approach
No surprises

## Slide 37
QUESTIONS ?

## Slide 38: FALL PROTECTION

## Slide 39
Making the rooftop a safer environment

## Slide 40: OSHA 1926.501 – Duty to have fall protection
1926.501(b)(1)
"Unprotected sides and edges." Each employee on a walking/working surface (horizontal and vertical surface) with an unprotected side or edge which is 6 feet (1.8 m) or more above a lower level shall be protected from falling by the use of guardrail systems, safety net systems, or personal fall arrest systems.
1926.501(b)(4)(i)
Each employee on walking/working surfaces shall be protected from falling through holes (including skylights) more than 6 feet (1.8 m) above lower levels, by personal fall arrest systems, covers, or guardrail systems erected around such holes.

## Slide 41: Educational Facilities – The Challenges

## Slide 42: IN-ACTION

## Slide 45: GW31 Series guardrail system
Features
Aluminum Mill finish
Customizable to suit all applications
Can be top or side mounted
Custom color railing is available
Complies with OSHA regulations 29 CFR 1910.23 and 1926.502

## Slide 46: GW20 Modular walkway system

## Slide 47: STACCO Modular railing system
Features
Non-penetrating weighted base – No penetration of the roof
Four port base allows infinite positioning of the rail sections
Positive locking system secures rails to base
Complies with OSHA regulations 29 CFR 1910.23 and 1926.502
Toe board adaptors available
No intermediate counterweights required, reducing trip hazards
Working handles are cast into base for easy lifting and positioning
Custom color railing is available

## Slide 48: Crossovers, Stairs and Platforms

## Slide 49: Building Codes & Good Roofing Practices

## Slide 50: Building Code
The latest energy requirements, building code, and good practices related to roofing
The codes have changed since the late 70’s

## Slide 51
R-Value is a measure of thermal resistance
The International Energy Conservation Code (IECC)
Climate Zone 5 requires R-25
R-Value Requirements

## Slide 52: Roof Core Cuts

## Slide 53
During the initial evaluation, we found that the building needed additional R Value to meet the current building codes.

## Slide 54
Determine existing roof substrate including roof deck construction
Specify the proper materials to meet or exceed the fire code classification
Fire Code Compliance

## Slide 55: INSIDE INSPECTION

## Slide 56
Create Positive drainage to prevent ponding water
Remove saturated insulation to prevent mold growth
Use appropriate materials to comply with temperature restrictions
Properly designing edge securement
Install walk protection around HVAC units and roof access points
Good Roofing Practice

## Slide 57
QUESTIONS ?

## Slide 58
We utilize the latest technology in the industry to ensure….
  Safe working environment
  Quality workmanship for customer
  Customer operations are uninterrupted
The Cotterman Way

## Slide 59
Minimize the human error factor
Leaves a consistent water-tight weld on seams
Increased production rates
Great ergonomic tool for our employees
Robotic welder

## Slide 60
Provides superior wind uplift performance
No membrane fastener penetrations
Increased production rates
Another great ergonomic tool being utilized
Rhinobond Induction Weld Machine

## Slide 61: Factory Applied Tape
Uniform adhesive width and thickness
Reduces human error during seam installation
Increased production rates
Factory Applied Tape

## Slide 62: SHEET METAL SHOP
ES-1 Certification
Sheet Metal Shop
ANSI/SPRI ES-1 and UL Certified
Proper gauge, design, and fastening pattern to meet specific wind design standard

## Slide 63: Real-Time Database
Our service techs have access to the work order as they are called in along with building history
Tablets are utilized by the techs to retrieve and relay information in real-time
Real-Time Database

## Slide 64: Field ticket recieved by service tech

## Slide 65
Aerial image showing leak area

## Slide 66: SAMPLE INVOICE TO CUSTOMER
Sample invoice to customer

## Slide 67
Cotterman
Online Roof Database
History of all roofing activities, inspection reports, photos, drawings, recommendations
Preventative Maintenance Program
-Inspections
-PM work performed
-Minor Maintenance & Repair
New/Re-Roof
-Design Phase
-Construction Phase
-Field Quality Control
-Post Construction Service
Warranty Verification
-Status
-Managing issues

## Slide 68
QUESTIONS ?